## Slide 1: Mitigating Flood Hazards on Tribal Lands with Data Science
C. Jason Tinant, PhD Civil Engineering, 2024-09-13
Lightning Talk
2024 OLC Wazi Paha

## Slide 2: Problem statement
Floods are natural hazards
Human actions can intensify or mitigate the impacts of floods
Floodplain designation, ‘the 100 year floodplain’, reduces risks to lives and property
Floodplains have not yet been designated for many Reservation communities
My research aims are to:
  1) Develop a robust approach to estimate 100-year flood magnitudes by clustering streams with similar flood behaviors from across a wide geographic area
  2) Identify key drivers of flood behavior, such as elevation, climate, geography.

## Slide 3
Annual peak discharge data
and metadata
USGS NWIS database
Geography
data
USEPA Ecoregion database
Temperature & precip.
data
PRISM database
Remove regulated gages & gages with < 20 yr of record
Select High Plain & Great Plain Ecoregions
Cluster station skewness - Gaussian Mixture Model
Select best fit model - BIC
Normalize peak discharge by watershed area
Calculate station skewness
Visualize groups - tSNE
Confirm groups - Silhouette Sc. & Cal-Har Index
Identify key drivers - Elastic Net regression
Calculate regional skewness
Determine 100-yr flood for gages of interest — White Clay Creek
Import data
Clean data
Identify regions
Understand results
Apply results
Analysis approach